## Slide 1: Arduino : Introduction & Programming
Anurag Dwivedi & Rudra Pratap Suman

## Slide 2: What is an Arduino ?
Open Source electronic prototyping platform based on flexible easy to use hardware and software.

## Slide 3: Uses of Arduino

## Slide 4: Getting started with Programming

## Slide 5: Bare minimum code
void setup() { // put your setup code here, to run once:
}
void loop() { // put your main code here, to run repeatedly:
}

## Slide 6: Bare minimum code
setup : It is called only when the Arduino is powered on or reset. It is used to initialize variables and pin modes
loop : The loop functions runs continuously till the device is powered off. The main logic of the code goes here. Similar to while (1) for micro-controller programming.

## Slide 7: PinMode
A pin on arduino can be set as input or output by using pinMode function.
pinMode(13, OUTPUT); // sets pin 13 as output pin
pinMode(13, INPUT); // sets pin 13 as input pin

## Slide 8: Reading/writing digital values
digitalWrite(13, LOW); // Makes the output voltage on pin 13 , 0V
digitalWrite(13, HIGH); // Makes the output voltage on pin 13 , 5V
int buttonState = digitalRead(2); // reads the value of pin 2 in buttonState

## Slide 9: Analog to Digital Coversion
What is analog ?
It is continuous range of voltage values (not just 0 or 5V)
Why convert to digital ?
Because our microcontroller only understands digital.

## Slide 10: ADC in Arduino Uno

## Slide 11: Converting Analog Value to Digital

## Slide 12: Quantanization the signal

## Slide 13: ADC in Arduino
The Arduino Uno board contains 6 pins for ADC
10-bit analog to digital converter
This means that it will map input voltages between 0 and 5 volts into integer values between 0 and 1023

## Slide 14: Reading/Writing Analog Values
analogRead(A0); // used to read the analog value from the pin A0
analogWrite(2,128);

## Slide 15: ADC Example
// These constants won't change. They're used to give names to the pins used: const int analogInPin = A0; // Analog input pin that the potentiometer is attached to const int analogOutPin = 9; // Analog output pin that the LED is attached to int sensorValue = 0; // value read from the pot int outputValue = 0; // value output to the PWM (analog out) void setup() { // initialize serial communications at 9600 bps: Serial.begin(9600); } void loop() { // read the analog in value: sensorValue = analogRead(analogInPin); // map it to the range of the analog out: outputValue = map(sensorValue, 0, 1023, 0, 255); // change the analog out value: analogWrite(analogOutPin, outputValue); // print the results to the serial monitor: Serial.print("sensor = " ); Serial.print(sensorValue); Serial.print("\t output = "); Serial.println(outputValue); // wait 2 milliseconds before the next loop // for the analog-to-digital converter to settle // after the last reading: delay(2); }