## Slide 1
“Heroes are made by the paths they choose, not the powers they are graced with.” – Tony Stark

## Slide 2
Notes: Look up analog ref

## Slide 3: Concepts: Analog vs. Digital
Microcontrollers are digital devices – ON or OFF. Also called – discrete.
analog signals are anything that can be a full range of values. What are some examples? More on this later…
5 V
0 V
5 V
0 V

## Slide 4: Arduino Integrated Development Environment (IDE)
Two required functions / methods / routines:
void setup()
{
// runs once
}
void loop()
{
// repeats
}
error & status messages
Notes: Be sure to point out the what all of the buttons do.

## Slide 5: Settings: Tools  Serial Port
Your computer communicates to the Arduino microcontroller via a serial port  through a USB-Serial adapter.
Check to make sure that the drivers are properly installed.
Notes: All connections to computers- mice, printers etc use a serial port. Gotta pick the right one.

## Slide 6: Settings: Tools  Board
Next, double-check that the proper board is selected under the ToolsBoard menu.
Notes: All connections to computers- mice, printers etc use a serial port. Gotta pick the right one.

## Slide 7: Let’s get to coding…
Project #1 – Blink
  “Hello World” of Physical Computing
Turn LED ON
Wait
Turn LED OFF
Wait
Rinse & Repeat

## Slide 8: Comments, Comments, Comments
Comments are for you – the programmer and your friends…or anyone else human that might read your code.
// this is for single line comments
// it’s good to put a description at //the top and before anything ‘tricky’
/* this is for multi-line comments
Like this…
And this….
*/

## Slide 9: Breadboard

## Slide 10: Project #1: Wiring Diagram
Image created in Fritzing

## Slide 11: Three commands to know…
pinMode(pin, INPUT/OUTPUT);
ex: pinMode(13, OUTPUT);
digitalWrite(pin, HIGH/LOW);
ex: digitalWrite(13, HIGH);
delay(time_ms);
ex: delay(2500); //delay of 2.5 //sec.
// NOTE: -> commands are CASE-sensitive
Notes: Three commands to rule the world… or at least do 80% of cool Arduino projects.

## Slide 12: Concepts: Analog vs. Digital
To create an analog signal, the microcontroller uses a technique called PWM. By varying the duty cycle, we can mimic an “average” analog voltage.
Pulse Width Modulation (PWM)

## Slide 13: Project #2– Fading Introducing a new command…
analogWrite(pin, val);
pin – refers to the OUTPUT pin (limited to pins 3, 5, 6, 9, 10, 11.) – denoted by a ~ symbol
val – 8 bit value (0 – 255).
0 => 0V | 255 => 5V

## Slide 14: Using Serial Communication
Method used to transfer data between two devices.
Arduino dedicates Digital I/O pin # 0 to receiving and Digital I/O pin #1 to transmit.
Data passes between the computer and Arduino through the USB cable. Data is transmitted as zeros (‘0’) and ones (‘1’) sequentially.
Notes: For this reason, we typically do not use Digital I/O 0 or 1 for anything in our designs.

## Slide 15: Serial Monitor & Serial Plotter
Initializes the Serial Communication
9600 baud data rate
prints data to serial bus

## Slide 16: Serial Monitor & Serial Plotter
Opens up a Serial Terminal Window

## Slide 17: Sensor vs Transducer

## Slide 18: Digital & Analog Sensors
Digital sensors are more straight forward than Analog
No matter what the sensor there are only two settings: On and Off
eg: PIR sensor, IR sensor, a Push Button.
The values of Analog sensors varies according to the resolution of sensor.
Signal is always in form of some analog voltage.
Eg. load cell, Hall Effect Sensors, Magnetic Sensors, Pressure Sensors, Load cell, Temperature Sensor, Solar Sensor, Humidity Sensor, Air Quality Sensor, Light Sensor, Rainfall Sensor, Soil moisture, Water Sensor

## Slide 19: analogRead()
Arduino uses a 10-bit A/D Converter:
this means that you get input values from 0 to 1023
  0 V  0
  5 V  1023
Ex:
int sensorValue = analogRead(A0);

## Slide 20
Project #3: Light Dependent Resistor [LDR]

## Slide 21: Potentiometer [Variable Resistor]

## Slide 22: Push Button/ Tactile Switch
to Digital Pin 2

## Slide 23: Project #4: Button Interfacing and concept of debouncing

## Slide 24: Concept of Debouncing

## Slide 25: Project #5: Temperature Sensing

## Slide 27
INTERRUPT INTERRUPT EVERYWHERE!

## Slide 28: Project #6: Infrared Sensor interfacing

## Slide 29: Infrared Sensor application

## Slide 30: Project #7: Servo Motor [SG90]

## Slide 31: Working of Servo Motor [SG90]

## Slide 32: Servo Motor [SG90] Interfacing Diagram

## Slide 33: Ultrasonic Sensor

## Slide 34: Ultrasonic Sensor interfacing with Arduino

## Slide 35: A Passive Infrared Sensor (PIR sensor)

## Slide 36: A Passive Infrared Sensor interfacing

## Slide 37
A Passive Infrared Sensor interfacing

## Slide 38: Great Audience
“Heroes are made by the paths they choose, not the powers they are graced with.” – Tony Stark